## Slide 1: DNS and IPv6
Geoff Huston
Joao Damas
APNIC Labs

## Slide 2: This is not a talk about DoH and DoT
For over a year DoH is still the current hot topic in the DNS
  and there is much that can be said about DoH and DoT
But let’s talk about something different but familiar at the same time
I want to get back to a much older but still not well understood issue in the DNS …

## Slide 3: Dual Stack DNS
How well is IPv6 supported in the DNS?
How does the DNS handle dual-stacked authoritative servers?
  Is there a “happy eyeballs” version of DNS server selection?
  Or is there a reverse bias to use IPv4?
If you placed authoritative servers on an IPv6-only service how many users would be able to reach you?
And what about DNSSEC?
  How well does IPv6 support large UDP packets?

## Slide 4: A word or two about “how” to talk about the DNS
We really don’t understand what a “resolver” is!
  It could be a single platform running an instance of DNS resolver code
  It could be a collection of independent back-end systems with a load distributor front end facing clients
  It could be a hybrid collection where the back ends synchronise each other to emulate a common cache
  It is a stub, recursive, or forwarding resolver
  A resolver may have 1 client or millions of clients or anything in between
When we talk about “resolvers” its challenging to understand exactly what we are talking about!

## Slide 5: Another word, this time about “how” to talk about DNS queries
We don’t understand what a query is!
  Which sounds silly, but the distributed resolution process causes a ‘fan out’ of queries as part of the resolution process when a single query may cause a number of ‘discovery’ queries to establish the identify of the authoritative server(s) for the name
  Resolvers all use their own timers for retransmission
  Queries have no “hop count” or “resolver path” attached
  there is no context to understand the reason for a query!
  Queries have a life of their own

## Slide 6: APNIC’s DNS Experimental Rig
Authoritative Server
Dual Stack
Recursive Resolver
Stub
Resolver
We instrument the Authoritative Server
We insert “known” DNS queries into the stub resolver
We make parts of the name unique to each experiment
That way the recursive resolvers have no cached data and are forced to query the authoritative server
We “see” the recursive to authoritative query process by instrumenting the authoritative server, and match experiment placement records to the server’s DNS logs

## Slide 7: Dual Stack DNS
How well is IPv6 supported in the DNS?
How does the DNS handle dual-stacked authoritative servers?
  Is there a “happy eyeballs” version of DNS server selection?
  Or is there a reverse bias to use IPv4?
If you placed authoritative servers on an IPv6-only service how many users would be able to reach you?
And what about DNSSEC?
  How well does IPv6 support large UDP packets?

## Slide 8: Dual Stack DNS
A “happy eyeballs*” DNS approach would be to prefer to use the IPv6 address of the authoritative server in preference to the IPv4 address
A “reverse bias” DNS approach would be to prefer to use the IPv4 address
* Why is happy eyeballs important?

## Slide 9: Dual Stack DNS
A “happy eyeballs*” DNS approach would be to prefer to use the IPv6 address of the authoritative server in preference to the IPv4 address
A “reverse bias” DNS approach would be to prefer to use the IPv4 address
IPv4 Only – 67%
IPv6
15%
IPv4+
IPv6
18%
* Why is happy eyeballs important?

## Slide 10: Dual Stack DNS
What’s going on here?
Time series of V4 / V6 query rates

## Slide 11: Dual Stack DNS
Time series of V4 / V6 query rates
Where we see both IPv4 and IPv6 used to query the authoritative server, there is a small bias to prefer to use IPv4 for the first query

## Slide 12: Dual Stack DNS
How well is IPv6 supported in the DNS?
How does the DNS handle dual-stacked authoritative servers?
  Is there a “happy eyeballs” version of DNS server selection?
  Or is there a reverse bias to use IPv4?
If you placed authoritative servers on an IPv6-only service how many users would be able to reach you?
And what about DNSSEC?
  How well does IPv6 support large UDP packets?
No!
Yes!

## Slide 13: Dual Stack DNS
How well is IPv6 supported in the DNS?
How does the DNS handle dual-stacked authoritative servers?
  Is there a “happy eyeballs” version of DNS server selection?
  Or is there a reverse bias to use IPv4?
If you placed authoritative servers on an IPv6-only service how many users would be able to reach you?
And what about DNSSEC?
  How well does IPv6 support large UDP packets?
No!
Yes!

## Slide 14: Dual Stack vs IPv6 only DNS
No query – 45%
IPv6 – 55%
IPv6 Only Test
In this case the authoritative name server only has an IPv6 address
Of all the clients that are presented with an experiment (41M over 5 days) 55% of names are seen asking for the experiment name over IPv6

## Slide 15: Dual Stack vs IPv6 only DNS
IPv4 Only – 67%
IPv6
15%
IPv4+
IPv6
18%
No query – 45%
IPv6 – 55%
IPv6 Only Test
Dual Stack

## Slide 16: Dual Stack DNS
How well is IPv6 supported in the DNS?
How does the DNS handle dual-stacked authoritative servers?
  Is there a “happy eyeballs” version of DNS server selection?
  Or is there a reverse bias to use IPv4?
If you placed authoritative servers on an IPv6-only service how many users would be able to reach you?
And what about DNSSEC?
  How well does IPv6 support large UDP packets?
No!
Yes!
55%

## Slide 17: Dual Stack DNS
How well is IPv6 supported in the DNS?
How does the DNS handle dual-stacked authoritative servers?
  Is there a “happy eyeballs” version of DNS server selection?
  Or is there a reverse bias to use IPv4?
If you placed authoritative servers on an IPv6-only service how many users would be able to reach you?
And what about DNSSEC?
  How well does IPv6 support large UDP packets?
No!
Yes!
55%

## Slide 18: IPv6 and Packet Fragmentation
IPv6 made two major changes to IP’s handling of packet fragmentation:
The fragmentation control header has been moved out of the IP header to become an extension header
  In other words the UDP / TCP protocol header is pushed further into the packet and to find it you need to follow the header chain
The IPv4 ‘Don’t Fragment’ bit is jammed on in IPv6
  In the case of path MTU issues IPv6 routers should not perform fragmentation on the fly, but are required to pass an ICMPv6 PTB message back to the packet’s sender

## Slide 19: Who uses Fragmentation anyway?
Well, the DNS is a good place to start looking!

## Slide 20: Who uses large DNS packets anyway?
Well, the DNS is a good place to start looking!
$ dig +dnssec DNSKEY org
; <<>> DiG 9.8.3-P1 <<>> +dnssec DNSKEY org
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 21353
;; flags: qr rd ra ad; QUERY: 1, ANSWER: 7, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags: do; udp: 512;
; QUESTION SECTION:
;org. IN DNSKEY
;; ANSWER SECTION:
org. 861 IN DNSKEY 256 3 7 AwEAAXxsMmN/JgpEE9Y4uFNRJm7Q9GBwmEYUCsCxuKlg
org. 861 IN DNSKEY 256 3 7 AwEAAayiVbuM+ehlsKsuAL1CI3mA+5JM7ti3VeY8ysmo
org. 861 IN DNSKEY 257 3 7 AwEAAZTjbIO5kIpxWUtyXc8avsKyHIIZ+LjC2Dv8naO+
org. 861 IN DNSKEY 257 3 7 AwEAAcMnWBKLuvG/LwnPVykcmpvnntwxfshHlHRhlY0F
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 3947
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 9795
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 17883
;; Query time: 134 msec
;; SERVER: 8.8.8.8#53(8.8.8.8)
;; WHEN: Mon Jul 31 12:07:16 2017
;; MSG SIZE rcvd: 1625
The response to a DNSKEY query for .org used a response of 1,625 octets!

## Slide 21: Who uses large DNS packets anyway?
Well, the DNS is a good place to start looking!
$ dig +dnssec DNSKEY org
; <<>> DiG 9.8.3-P1 <<>> +dnssec DNSKEY org
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 21353
;; flags: qr rd ra ad; QUERY: 1, ANSWER: 7, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags: do; udp: 512;
; QUESTION SECTION:
;org. IN DNSKEY
;; ANSWER SECTION:
org. 861 IN DNSKEY 256 3 7 AwEAAXxsMmN/JgpEE9Y4uFNRJm7Q9GBwmEYUCsCxuKlg
org. 861 IN DNSKEY 256 3 7 AwEAAayiVbuM+ehlsKsuAL1CI3mA+5JM7ti3VeY8ysmo
org. 861 IN DNSKEY 257 3 7 AwEAAZTjbIO5kIpxWUtyXc8avsKyHIIZ+LjC2Dv8naO+
org. 861 IN DNSKEY 257 3 7 AwEAAcMnWBKLuvG/LwnPVykcmpvnntwxfshHlHRhlY0F
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 3947
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 9795
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 17883
;; Query time: 134 msec
;; SERVER: 8.8.8.8#53(8.8.8.8)
;; WHEN: Mon Jul 31 12:07:16 2017
;; MSG SIZE rcvd: 1625
The response to a DNSKEY query for .org used a response of 1,625 octets!
That was back in 2017 – what about today?
$ dig +dnssec DNSKEY org
; <<>> DiG 9.16.2 <<>> +dnssec DNSKEY org
;; global options: +cmd
;; Got answer:
…
;; WHEN: Sat May 02 13:22:02 AEST 2020
;; MSG SIZE rcvd: 1058

## Slide 22: Who uses large DNS packets anyway?
Well, the DNS is a good place to start looking!
$ dig +dnssec DNSKEY org
; <<>> DiG 9.8.3-P1 <<>> +dnssec DNSKEY org
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 21353
;; flags: qr rd ra ad; QUERY: 1, ANSWER: 7, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags: do; udp: 512;
; QUESTION SECTION:
;org. IN DNSKEY
;; ANSWER SECTION:
org. 861 IN DNSKEY 256 3 7 AwEAAXxsMmN/JgpEE9Y4uFNRJm7Q9GBwmEYUCsCxuKlg
org. 861 IN DNSKEY 256 3 7 AwEAAayiVbuM+ehlsKsuAL1CI3mA+5JM7ti3VeY8ysmo
org. 861 IN DNSKEY 257 3 7 AwEAAZTjbIO5kIpxWUtyXc8avsKyHIIZ+LjC2Dv8naO+
org. 861 IN DNSKEY 257 3 7 AwEAAcMnWBKLuvG/LwnPVykcmpvnntwxfshHlHRhlY0F
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 3947
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 9795
org. 861 IN RRSIG DNSKEY 7 1 900 20170815152632 20170725142632 17883
;; Query time: 134 msec
;; SERVER: 8.8.8.8#53(8.8.8.8)
;; WHEN: Mon Jul 31 12:07:16 2017
;; MSG SIZE rcvd: 1625
The response to a DNSKEY query for .org used a response of 1,625 octets!
That was back in 2017 – what about today?
$ dig +dnssec DNSKEY org
; <<>> DiG 9.16.2 <<>> +dnssec DNSKEY org
;; global options: +cmd
;; Got answer:
…
;; WHEN: Sat May 02 13:22:02 AEST 2020
;; MSG SIZE rcvd: 1058
.org may have dropped its response size for DNSKEY queries
but there are still very large entries for other TLDs

## Slide 23: Who uses large DNS packets anyway?
.booking 2932
.winners 2932
.watches 2932
.ferrero 2932
.lincoln 2932
.chintai 2932
.citadel 2932
.oldnavy 2932
.banamex 2932
.farmers 2932
.athleta 2932
.jpmorgan 2937
.discover 2937
.homegoods 2942
.marshalls 2942
.analytics 2942
.homesense 2942
.statefarm 2942
.swiftcover 2947
.xn--kpu716f 2952
.weatherchannel 2967
.bananarepublic 2967
.americanexpress 2972
.gdn 3033
Size of dnssec-signed DNSKEY response for some gtlds
These folk do!

## Slide 24: Who uses large DNS packets anyway?
Some 300 gtlds rely on fragmented UDP responses!

## Slide 25: However…
UDP Fragmentation has its problems
  UDP trailing fragments in IPv4 and IPv6 may encounter fragment filtering rules on firewalls in front of resolvers
  Large UDP packets in IPv6 may encounter path MTU mismatch problems, and the ICMP6 Packet Too Big diagnostic message may be filtered.
    Even if it is delivered, the host may not process the message due to the lack of verification of the authenticity of the ICMP6 message.
    Because the protocol is UDP, receipt of an ICMP6 message will not cause retransmission of a re-framed packet.
  UDP fragments in IPv6 are implemented by Extension Headers. There is some evidence of deployment of IPv6 switching equipment that unilaterally discards IPv6 packets with extension headers

## Slide 26: Is this a problem for today’s IPv6 Internet?
Can we measure the extent to which users might be affected with this scenario of large DNS responses, DNS resolvers and IPv6?

## Slide 27: Our Measurement Approach
We use an Online Ad platform to enroll endpoints to attempt to resolve a set of DNS names:
  Each endpoint is provided with a unique name string (to eliminate the effects of DNS caching)
  The DNS name is served from our authoritative servers
  Resolving the DNS name requires the user’s DNS resolvers to receive a fragmented IPv6 packet

## Slide 28: V6, the DNS and Fragmented UDP
Total number of tests (DNS over UDP over IPv6): 27,619,047
Failure Rate in receiving a large response: 11,232,833
IPv6 Fragmentation Failure Rate: 41%
Data gathered 26 April – 1 May 2020

## Slide 29: V6, the DNS and Fragmented UDP
Total number of tests (DNS over UDP over IPv6): 27,619,047
Failure Rate in receiving a large response: 11,232,833
IPv6 Fragmentation Failure Rate: 41%
Data gathered 26 April – 1 May 2020
That’s awesomely bad!

## Slide 30: What to do?
Accepting a future IPv6-only Internet means we are going to have to take the problem of IPv6 Fragmentation seriously
  Because relying on IPv4 as a backup is a hack with an indeterminate future!
Which means that we need to figure out how to change the appalling drop rate for fragmented IPv6 packets both in the DNS and in end-to-end paths in the net
  Should we try and fix the network problem or try to work around it?

## Slide 31: What do the RFC’s say?

## Slide 32: What do the RFC’s say?

## Slide 33: What do the RFC’s say?

## Slide 34: What do the RFC’s say?
This BCP is saying that using EDNS(0) in the DNS to signal the capability of accepting large fragmented DNS responses was unwise, and if a host/application does not know the path MTU, it should truncate at UDP at 1280 octets (and IPv4 should truncate at 512 octets!)
DON’T FRAGMENT!

## Slide 35: What can we do about it?
Fix it!
Get all the deployed routers, switches and firewalls and related network middleware to accept packets with IPv6 Fragmentation Headers

## Slide 36: What can we do about it?
Fix it!
Get all the deployed routers, switches and firewalls and related network middleware to accept packets with IPv6 Fragmentation Headers

## Slide 37: What can we do about it?
Change it!
Change the way in which IPv6 manages IP fragmentation and the use of Extension Headers as Fragmentation Control fields

## Slide 38: What can we do about it?
Change it!
Change the way in which IPv6 manages IP fragmentation and the use of Extension Headers as Fragmentation Control fields

## Slide 39: What can we do about it?
Avoid it!
Change application behaviour to avoid the use of packet fragmentation completely

## Slide 40: What can we do about it?
Avoid it!
Change application behaviour to avoid the use of packet fragmentation completely

## Slide 41: Which?
All of these options have a certain level of pain, cost and potential inconvenience
Its hard to work out what is the best course of action, but it seems like a lot of extra effort if we take on all three at once!

## Slide 42: Large DNS Responses and IPv6
Change the transport protocol?
  DNS over TCP by default
  DNS over TLS over TCP by default
  DNS over HTTP over TLS over TCP
  DNS over QUIC
  Devise some new DNS framing protocol that uses multiple packets with firewall-friendly packet and protocol headers instead of IP fragmentation

## Slide 43: Large DNS Responses and IPv6
Change the application protocol behaviour?
  Perform UDP MTU discovery using EDNS(0) UDP Buffer Size variations as a probe
  Shift Additional Records into additional explicit UDP query/response transactions rather than bloating the original DNS response
  Add a truncated minimal UDP response to trail a fragmented response (ATR)

## Slide 44: Where now?
We have a decent idea of the problem space we need to resolve
We’d prefer a plan that allows each of us to work independently rather than a large scale orchestrated common change
We’re not sure we can clean up all the ICMPv6 filters and EH packet droppers in the IPv6 network
And it sure seems a bit late in the day to contemplate IPv6 protocol changes
Which means that we are probably looking at working around the problem by changing the behaviour of DNS and use an upper payload size of 1232 octets
See https://dnsflagday.net/2020/

## Slide 45
Thanks!

## Slide 46: Additional Material

## Slide 47: Top 20 Tables

## Slide 48: Which Resolvers?
73,354 IPv6 resolver /48 subnets seen
12,287 resolvers were consistently unable to resolve the target name (likely due to failure to receive the fragmented response)
Which is too large a list to display here
But we can show the top 20…

## Slide 49: Which Resolvers can’t
All these resolvers appear to be unable to receive fragmented UDP
This is the top 20, as measured by the number of tests that used this resolver subnet
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 50: Which Network’s Resolvers can’t
All these networks host resolvers that appear to be unable to receive fragmented UDP
This is the Top 20, as measured by the query count per origin AS of the resolver address
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 51: Its not quite so simple as “can’t”
When a resolver fails to receive a UDP response it _may_ re-query with a smaller UDP buffer size
parameter
This will cause our server to respond with a truncated DNS response over UDP
This _should_ cause the resolver to re-query using TCP
resolver
server
1. Large fragmented UDP
2. Truncated unfragmented UDP
3. TCP
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 52: It’s not quite so simple as “can’t”
When a resolver fails to receive a UDP response it _may_ re-query with a smaller UDP buffer size
parameter
This will cause our server to respond with a truncated DNS response over UDP
This _should_ cause the resolver to re-query using TCP
There are four cases of fragmentation failure :
can’t receive fragmented UDP and won’t use a smaller UDP Buffer Size
can’t receive fragmented UDP, will use a smaller UDP Buffer Size but cannot make a TCP connection
can’t receive fragmented UDP, will use a smaller UDP Buffer Size but cannot complete a TCP connection
can’t receive fragmented UDP, will use a smaller UDP Buffer Size and make a TCP connection (fail then recovery)
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 53: Case 1 - Which Resolvers really can’t
These resolvers appear to be unable to receive fragmented UDP and will not re-query with a smaller UDP buffer size
This is the Top 20, as measured by the query count per resolver subnet address
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 54: Case 1 - Which Networks’ Resolvers really can’t
These networks host resolvers that appear to be unable to receive fragmented UDP and will not re-query with a
smaller UDP buffer size
This is the Top 20, as measured by the query count per ASN
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 55: Case 2 - Which Resolvers can’t TCP
These resolvers appear to be unable to receive fragmented UDP, will re-query with a smaller UDP buffer size but not open a TCP session
This is the top 20, as measured by the query count per resolver subnet address
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 56: Case 2 - Which Networks’ Resolvers can’t TCP
These networks host resolvers that appear to be unable to receive fragmented UDP, will re-query with a smaller UDP buffer size but not open a TCP session
This is the top 20, as measured by the query count per resolver subnet address
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 57: Case 3 - Which Resolvers can’t complete TCP
These resolvers appear to be unable to receive fragmented UDP, will re-query with a smaller UDP buffer size, will open a TCP session, but appear to have a TCP MTU black hole issue
This is the top 20, as measured by the query count per resolver subnet address
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 58: Case 3 - Which Networks’ Resolvers can’t complete TCP
These networks host resolvers that appear to be unable to receive fragmented UDP, will re-query with a smaller UDP buffer size, will open a TCP session, but appear to have a TCP MTU black hole issue
This is the top 20, as measured by the query count per resolver subnet address
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 59: Case 4 - Which Resolvers can’t Frag but can TCP
These resolvers appear to be unable to receive fragmented UDP, will re-query with a smaller UDP buffer size, get the truncated UDP response and successfully complete the TCP session
This is the top 20, as measured by the query count per resolver subnet address
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more

## Slide 60: Case 4 - Which Networks’ Resolvers can’t Frag but can TCP
These networks host resolvers that appear to be unable to receive fragmented UDP, will re-query with a smaller UDP buffer size, get the truncated UDP response and successfully complete the TCP session
This is the top 20, as measured by the query count per resolver subnet address
Notes: ./count-rvrs.pl | originas -d ' ' -f 1 | originas -d ' ' -f 1 -n | more