## Slide 1: Satellite Broadband in the Asia Pacific
Panel Session
Geoff Huston
APNIC

## Slide 2: Why use Satellite services?
We have deployed so much undersea fibre in the past couple of decades! Why does the region need more capacity?
https://www.submarinecablemap.com/

## Slide 3: Submarine Route Choke Points
Hazards for submarine cables include:
Landings at busy port locations (Singapore, Hong Kong)
Shallow water (South China Sea)
Active Plate boundaries (Luzon Strait, Japan East Coast, Sunda Arc)
Political Tensions (Hong Kong, Shanghai, South China Sea)

## Slide 4
https://commons.wikimedia.org/wiki/File:Orbitalaltitudes.jpg GNU Free Documentation License
Satellites: GEOs and LEOs

## Slide 5: Geostationary Earth Orbit
At an altitude of 35,786km a satellite will orbit the earth with the same period as the earth’s rotation – from the earth it will appear to be stationary in the sky
https://secure.boeingimages.com/archive/Commercial-Communications-Satellites-Orbit-2F3XC5KQCM9.html
https://commons.wikimedia.org/wiki/File:Communications_satellite_with_TEMPO_spacecraft_model.png – public domain

## Slide 6: GEO Services
Requires earth station investment
Limited capacity
  Limited orbital slots
  Constrained frequency allocation
High delay
  Challenging for network use
Remote Reach

## Slide 7
Low Earth Orbit
https://commons.wikimedia.org/wiki/File:Orbitalaltitudes.jpg GNU Free Documentation License

## Slide 8: Leo Services
Historically high launch costs
  This has changed significantly with SpaceX reusable launch vehicles
High angular velocity, small footprint
  Requires active tracking and inter-satellite handover
  Requires a large constellation to provide continuous service
Regulatory hurdles
  Terrestrial licenses

## Slide 9: LEO Constellations: Starlink
3,773 satellites, 3,129 in service (Planned total: 12,000)
inclined orbit (53O), 550km
Retail Services
Satellite-to-Satellite coming with V2 satellites
2022
2023
3,000
2,000
1,000
Starlink Satellite Map (from https://satellitemap.space)

## Slide 10: LEO Constellations: Oneweb
542 operational satellites (planned total: 648)
polar orbit, altitude: 1,200km, business and government clients

## Slide 11: LEO Constellations: Project Kuiper (Amazon)
Currently still in planning
3,276 planned satellites, altitude: 590km,610km, 630km
Planned retail services

## Slide 12: Others
China?
Others?

## Slide 13: LEOs
It’s a big money play, and without the ability to make head roads into high value service markets its probably an exercise with no prospect of a positive cash flow
  Remember Iridium?
  And Oneweb has already gone bankrupt once!
Is this a niche market or a massive game changer for terrestrial access services?

## Slide 14: Today’s Panel
Dan York, ISOC – overview of issues and concerns
Dr Ulrich Speidel, Univ Auckland – Pacific Experiences with satellite services
Mike Puchol, Africa Rural and Remote – challenging environments in Africa
Debopam Bhattacherjee, Microsoft Research – model of satellite-to-satellite SDN routing