## Slide 1: On LEOs and Starlink
Geoff Huston AM
Chief Scientist, APNIC
November 2023

## Slide 2
screenshot from starwatch app
Screenshot: https://asia.nikkei.com/Business/Telecommunication/Elon-Musk-s-Starlink-launches-satellite-internet-service-in-Japan
Screenshot - https://www.theverge.com/2022/8/25/23320722/spacex-starlink-t-mobile-satellite-internet-mobile-messaging
LEOs in the News

## Slide 3: Newtonian Physics
If you fire a projectile with a speed greater than 11.2Km/sec it will not fall back to earth, and instead head away from earth never to return
On the other hand, if you incline the aiming trajectory and fire it at a critical speed it will settle into an orbit around the earth
The higher the altitude, the lower the orbital speed required to maintain orbit

## Slide 4: Solar Radiation Physics
The rotating iron core of the Earth produces a strong magnetic field
This magnetic deflects solar radiation – the Van Allen Belt
Sheltering below the Van Allen Belt protects the spacecraft from the worst effects of solar radiation, allowing advanced electronics to be used in the spacecraft

## Slide 5
Low Earth Orbit
https://commons.wikimedia.org/wiki/File:Orbitalaltitudes.jpg GNU Free Documentation License

## Slide 6: Low Earth Orbit
LEO satellites are stations between 160km and 2,000km in altitude.
High enough to stop it slowing down by “grazing” the denser parts of the earth’s ionosphere
Not so high that it loses the radiation protection afforded by the Inner Van Allen belt.
At a height of 550km, the minimum signal propagation delay to reach the satellite and back is 3.7ms, at 25o it’s 7.5ms, and at the horizon it’s 18ms
screenshot from starwatch app
Image - spacex

## Slide 7: Starlink Constellation
If you use a minimum angle of elevation of 25o then at an altitude of 550km each satellite spans a terrestrial footprint of no more than ~900Km radius, or 2M K2
At a minimum, a LEO satellite constellation needs 500 satellites to provide coverage of all parts of the earth’s surface
For high quality coverage the constellation will need 6x-20x that number (or more!)

## Slide 8: Starlink Constellation
4,276 in-service operational spacecraft, operating at an altitude of 550km
https://satellitemap.space/

## Slide 9: So LEOs are “interesting”!
They are very close to the Earth – which means:
  They don’t need specialised high-power equipment to send and receive signals
    Even hand-held mobile devices can send and receive signals with a LEO!
  They can achieve very high signal speeds
    It’s a highly focussed signal beam
  They are harder to disrupt by external interference
But you need a large number of them to provide a continuous service
The extremely host cost of launching a large constellation of LEO spacecraft has been the major problem with LEO service until recently
  Which is why Motorola’s Iridium service went bankrupt soon after launch

## Slide 10: What’s changed recently?
SpaceX’s reusable rocket technology has slashed the cost of lifting spacecraft into low earth orbit
SpaceX
https://ourworldindata.org/grapher/cost-space-launches-low-earth-orbit
Cost/Kg (log scale)
Time

## Slide 11
Current and Planned satellite constellations

## Slide 12: Tracking a LEO satellite
550km
27,000 km/h
Satellite
horizon to horizon: ~5 minutes

## Slide 13: Looking Up
Starlink tracks satellites with a minimum elevation of 25o.
There are between 30 – 50 visible Starlink satellites at any point on the surface between latitudes 56o North and South
Each satellite traverses the visible aperture for a maximum of ~3 minutes

## Slide 14: Starlink Scheduling
A satellite is assigned to a user terminal in 15 second time slots
Tracking of a satellite (by phased array focussing) works across 11 degrees of arc per satellite in each 15 second slot
client
11o
15 seconds

## Slide 15: Starlink Scheduling
Latency changes on each satellite switch
If we take the minimum latency on each 15 second scheduling interval, we can expose the effects of the switching interval on latency
Across the 15 second interval there will be a drift in latency according to the satellite’s track and the distance relative to the two earth points
Other user traffic will also impact on latency, and also the effects of a large buffer in the user modem

## Slide 16: Starlink Spot Beams
Each spacecraft 2,000 MHz of spectrum for user downlink and splits it into 8x channels of 250 MHz each
Each satellite has 3 downlink antennas and 1 uplink antennas, and each can do 8 beams x 2 polarizations, for a total of 48 beams down and 16 up.
“Unveiling Beamforming Strategies of Starlink LEO Satellites”
https://people.engineering.osu.edu/sites/default/files/2022-10/Kassas_Unveiling_Beamforming_Strategies_of_Starlink_LEO_Satellites.pdf

## Slide 17: Starlink’s reports
$ starlink-grpc-tools/dish_grpc_text.py -v status
id: ut01000000-00000000-005dd555
hardware_version: rev3_proto2
software_version: 5a923943-5acb-4d05-ac58-dd93e72b7862.uterm.release
state: CONNECTED
uptime: 481674
snr:
seconds_to_first_nonempty_slot: 0.0
pop_ping_drop_rate: 0.0
downlink_throughput_bps: 16693.330078125
uplink_throughput_bps: 109127.3984375
pop_ping_latency_ms: 49.5
Alerts bit field: 0
fraction_obstructed: 0.04149007424712181
currently_obstructed: False
seconds_obstructed:
obstruction_duration: 1.9579976797103882
obstruction_interval: 540.0
direction_azimuth: -42.67951583862305
direction_elevation: 64.61225128173828
is_snr_above_noise_floor: True

## Slide 18: Reported Capacity & Latency

## Slide 19: Reported Capacity & Latency
This is going to present some interesting issues for conventional TCP
TCP uses ACK pacing which means it attempts to optimize its sending rate over multiple RTT intervals
The variation in latency and capacity occurs at high frequency, which means that TCP control is going to struggle to optimize itself against a shifting target

## Slide 20: Link Characteristics
1-second ping
Micro-drops
Highly unstable jitter
24 Hours

## Slide 21: How well does all this work?
Speedtest measurements:
We should be able to get ~120Mbps out of a starlink connection. Right?

## Slide 22: TCP Flow Control Algorithms
“Ideal” Flow behaviour for each protocol

## Slide 23: iperf3 – cubic, 60 seconds
CUBIC
Loss

## Slide 24: Qperf – quic (with cubic)
QUIC/CUBIC
Loss

## Slide 25: iperf3 - bbr
BBR
Loss

## Slide 26: Cubic, Quic/Cubic, BBR

## Slide 27: Protocol Considerations
Starlink services have two issues:
  Very high jitter rates
  High levels of micro-loss
Loss-based flow control algorithms will over-react and pull back the sending rate over time
  Short transactions work very well
  Paced connections (voice, zoom, video streaming) tend to work well most of the time
  Bulk data transfer, not so much
You need to move to less loss-sensitive flow control algorithms, such as BBR to get good performance out of these services

## Slide 28: What about Starlink Gen2?
These satellites are larger, heavier and operate at a higher power level
More bandwidth available, better SNR, and high achievable data speeds
Multiple orbital plans at a collection of discrete altitudes
Incorporates 5G cellular services
Will use inter-satellite laser connectors to support packet routing across satellites – few details as yet

## Slide 29: I don’t want to leave you with the wrong impression of Starlink
Starlink is perfectly acceptable for:
  short transactions
  video streaming
  conferencing
The service can sustain 10 – 20Mbps delivery for long-held sessions
  The isolated drop events generally do not intrude into the session state
And it can be used in all kinds of places where existing wire and mobile radio systems either under-perform or aren’t there at all!
Its probably not the best trunk infrastructure service medium, but it’s a really good high speed last mile direct retail access service, particularly for remote locations!
Its also very challenging to jam!

## Slide 30: Questions?