## Slide 1: Measuring Starlink Protocol Performance
Geoff Huston
APNIC

## Slide 2: From NANOG 92…

## Slide 3: From NANOG 92…

## Slide 4: From NANOG 92…
WHY does BBR outperform CUBIC on Starlink systems?

## Slide 5: Low Earth Orbit
LEO satellites are stations between 160km and 2,000km in altitude. Starlink operates at 550km (V2 includes additional orbital shells at 525km, 530km and 535km)
High enough to stop it slowing down by “grazing” the denser parts of the earth’s ionosphere
Not so high that it loses the radiation protection afforded by the Inner Van Allen belt.
At a height of 550km, the minimum signal propagation delay to reach the satellite and back is 3.7ms, at 25o elevation it’s 7.5ms.
screenshot from starwatch app
Image - spacex

## Slide 6: Starlink is “interesting”!
The spacecraft are very close to the Earth – which means:
  They don’t need specialised high-power equipment to send and receive signals
    Even hand-held mobile devices can send and receive signals with a LEO!
  They can achieve very high signal speeds *
    It’s an array of highly focussed signal beams
But you need a large number of satellites to provide a continuous service
The extremely high cost of launching a large constellation of LEO spacecraft has been the major problem with LEO service until recently
  (Which was a major reason why Motorola’s Iridium service went bankrupt soon after launch)
* Mobiles can’t achieve high speeds, but if you use an antenna then things improve dramatically!

## Slide 7: Starlink Architecture

## Slide 8: Tracking a LEO satellite
370km - 550km
27,000 km/h
Satellite
horizon to horizon: ~5 minutes

## Slide 9: Looking Up
Starlink tracks satellites with a minimum elevation of 25o.
There are between 30 – 50 visible Starlink satellites at any point on the surface between latitudes 56o North and South
Each satellite traverses the visible aperture for a maximum of ~3 minutes

## Slide 10: Starlink Scheduling
A satellite is assigned to a user terminal in 15 second time slots
Tracking of a satellite (by phased array focussing) works across 11 degrees of arc per satellite in each 15 second slot
client
11o
15 seconds

## Slide 11: Starlink Spot Beams
Each spacecraft uses 2,000 MHz of spectrum for user downlink and splits it into 8x channels of 250 MHz each
Each satellite has 3 downlink antennas and 1 uplink antennas, and each can do 8 beams x 2 polarizations, for a total of 48 beams down and 16 up.
“Unveiling Beamforming Strategies of Starlink LEO Satellites”
https://people.engineering.osu.edu/sites/default/files/2022-10/Kassas_Unveiling_Beamforming_Strategies_of_Starlink_LEO_Satellites.pdf

## Slide 12: Starlink’s Reports
$ starlink-grpc-tools/dish_grpc_text.py -v status
id: ut01000000-00000000-005dd555
hardware_version: rev3_proto2
software_version: 5a923943-5acb-4d05-ac58-dd93e72b7862.uterm.release
state: CONNECTED
uptime: 481674
snr:
seconds_to_first_nonempty_slot: 0.0
pop_ping_drop_rate: 0.0
downlink_throughput_bps: 16693.330078125
uplink_throughput_bps: 109127.3984375
pop_ping_latency_ms: 49.5
Alerts bit field: 0
fraction_obstructed: 0.04149007424712181
currently_obstructed: False
seconds_obstructed:
obstruction_duration: 1.9579976797103882
obstruction_interval: 540.0
direction_azimuth: -42.67951583862305
direction_elevation: 64.61225128173828
is_snr_above_noise_floor: True

## Slide 13: Reported Capacity & Latency

## Slide 14: Reported Capacity & Latency
Why is this service so unstable?

## Slide 15: Starlink Scheduling
Latency changes on each satellite switch
If we take the minimum latency on each 15 second scheduling interval, we can expose the effects of the switching interval on latency
Across the 15 second interval there will be a drift in latency according to the satellite’s track and the distance relative to the two earth points
Other user traffic will also impact on latency, and also the effects of a large buffer in the user modem

## Slide 16: Satellite handover
Each handover sees a spike in latency and a higher probability of loss

## Slide 17: Satellite handover
Packet loss occurs most frequently during handover events, and if confined to small set of packets
This is NOT congestion-based tail-drop loss - so the packet loss can be generally repaired by a TCP SACK mechanism without needing a TCP session restart
Loss
Latency

## Slide 18: Latency
The signal propagation latency to push a signal up and back to a Starlink spacecraft varies between 3.7ms and 7.5ms – which is an RTT of 7.4ms to 15ms
But the minimum RTTs we see are 20ms!
And the jitter is at an extremely high frequency (as is the change in channel capacity)

## Slide 19: Varying SNR means varying signal modulation
Starlink likely uses IEEE 802.11ac dynamic channel rate control, adjusting the signal modulation to match the current SNR
This continual adjustment causes continual shift in the available capacity and imposes a varying latency on the round-trip time
It also adds a few ms to the RTT times

## Slide 20: So What?
The variation in latency and capacity occurs at high frequency, which means that TCP control is going to struggle to optimize itself against a shifting target
TCP uses ACK pacing which means it attempts to optimize its sending rate over multiple RTT intervals

## Slide 21: Frames
Starlink does NOT provide each user with a dedicated frequency band
The system uses multiplexing to divide a channel into frames and sends 750 frames per second. Each frame is divided into 302 intervals.
Each frame carries a header that contains satellite, channel and modulation information

## Slide 22: Starlink Characteristics
Varying SNR produces varying modulation, which is expressed as varying capacity and delay
Relative motions of earth and spacecraft add to varying latency
15 second satellite handover generates regular loss and latency extension
Contention for common transmission medium leads to queuing delays

## Slide 23: In Summary…
The profile of a Starlink connection is governed by:
  Regular handovers at precise 15 second intervals when the connection will experience:
    a change in base latency
    very short-term additional queuing latency of ~80 – 100ms
    a high probability of non-congestion packet loss
  Adaptive dynamic rate control by constantly changing signal modulation
    High frequency jitter
    No consistent upper bound to channel capacity
  Common channel contention with other users

## Slide 24: How well does all this work?
Speedtest measurements:
We should be able to get ~160Mbps out of a Starlink connection.

## Slide 25: TCP Flow Control Algorithms
“Ideal” Flow behaviour for each protocol

## Slide 26: iperf3 – cubic, 40 seconds

## Slide 27: iperf3 – cubic, 40 seconds
Slow Start
Queue Drain
Congestion Avoidance

## Slide 28: iperf3 - bbr
Satellite handover

## Slide 29: Transport Protocol Considerations
Starlink services have three issues:
  Very high jitter rates – varying signal modulation
  High levels of micro-loss (1.4%) – largely due to loss on satellite handover events (every 15 seconds)
  Common bearer contention between users
Loss-based flow control algorithms will over-react and pull back the sending rate over time
  Short transactions work very well
  Paced connections (voice, zoom, video streaming) tend to work well most of the time
To obtain better performance you need to move to flow control algorithms that are not as loss-sensitive, such as BBR

## Slide 30: Other considerations
Senders should use fair queuing to pace sending rates and avoid bursting and tail drop behaviours
SACK (selective acknowledgement) for TCP can help in rapid repair to multiple lost packets
It’s likely that ECN would also be really helpful to the protocol to disambiguate latency changes due to satellite behaviours and network queue buildup - i.e. only shrink the congestion window in response to ECN signals, not packet loss!

## Slide 31: Starlink Performance
Starlink is perfectly acceptable for:
  short transactions
  video streaming
  conferencing
The service can sustain 40 – 50Mbps delivery for long-held sessions during local peak use times in high density use scenarios
  The isolated drop events generally do not intrude into the session state
In off-peak and/or low-density contexts it can deliver 200-300Mbps
Or, if the server uses BBR, then higher throughput is possible!
It can be used in all kinds of places where existing wire and mobile radio systems either under-perform or aren’t there at all!
Its probably not the best trunk infrastructure service medium, but it’s a really good high speed last mile direct retail access service, particularly for remote locations!

## Slide 32: Making Starlink Faster
Increase antennae transmitter power
Use higher gain antennae with narrower beams
Drop the orbital altitude to 340Km
Drop the minimum elevation angle from 25o to 20o
Use more bands (Ka-, V-, and E- bands)
(Proposed measures described in an October 2024 FCC application by Starlink)

## Slide 33: Questions?