## Slide 1: BGP in 2025
Geoff Huston
APNIC

## Slide 2: This presentation
IPv4 Routing Table
IPv6 Routing Table
FIB Projections
Updates and Churn
Conclusions

## Slide 3: 32 Years of Routing the IPv4 Internet – FIB Count
1994: Introduction of CIDR
2001: The Great Internet
Boom and Bust
2005: Consumer Market
2011: Onset of Address Exhaustion
This is a view pulled together from each of the routing peers of Route-Views and RIPE RIS
2020: The COVID Years

## Slide 4: IPv4 in 2025
The DFZ now exceeds 1M entries for ALL BGP peers
45K entry variation

## Slide 5: IPv4 in 2025
AS4155 – USDA
WDL 3,122 pfxs on 1-Nov

## Slide 6: IPv4 in 2025
?

## Slide 7: 7 July 2025 - Egypt
On July 7, 2025, a major fire broke out at the Ramses Central building in Cairo, a critical telecommunications hub. The fire resulted in four deaths, dozens of injuries, and significant disruptions to Egypt's internet and telecommunications services. The incident also led to a temporary suspension of trading on the Cairo stock exchange and caused severe traffic congestion due to street closures.
Daily News Egypt

## Slide 8: Announced Prefix Changes in 2025

## Slide 9: 32 Years of Routing the IPv4 Internet – Address Span
2001: The Great Internet
Boom and Bust
This is a view pulled together from each of the routing peers of Route-Views and RIPE RIS
2011: Onset of Address Exhaustion
2021: Advertised DoD blocks
2005: Consumer Market

## Slide 10: 2025 in Detail

## Slide 11: 2025 in Detail
4-Jan AS16509, Amazon, +4.3M
28-Feb AS37963, Alibaba Advertising, -3.5M
5-Mar AS16509, Amazon, +1.9M
28-Feb AS17676, Softbank GigInfra, -1.9M
28-Feb AS8100, Quadranet, -1.9M
4-May AS16509, Amazon, +4.6M
16 Jun, AS7738, V Tal, Brazil, -2.6M
16 Jun, AS6389, Bell South, -0.5M
18-Sep AS396982, Google Cloud, +3.2M
4-Nov AS16509, Amazon, -15.8M
10-Dec AS16509, Amazon, +15.1M

## Slide 12: AS16509 – Amazon in 2025

## Slide 13: 2025: Assigned vs Recovered Addresses
Change in UnAdvertised Addresses
Change in the Advertised Address Pool
RIR Allocations
3.1B advertised
-11M delta
580M unadvertised
+10M delta
3.7B assigned
-0.25M

## Slide 14: Announced Address Span Changes in 2025
The advertised table shrunk by 11M /32’s over 2025

## Slide 15: Announced Address Span Changes in 2025
The advertised table shrunk by 11M /32’s over 2025

## Slide 16: What Happened in 2025 in V4
The size of the FIB table is growing, but the span of advertised addresses is declining
V4 Address use in access networks is declining in some markets, notably the US
V4 address use in Cloud infrastructure is still increasing
Use of more specific entries in IPv4 fell from 52.9% of all advertised V4 prefixes to 51.8%

## Slide 17: This presentation
IPv4 Routing Table
IPv6 Routing Table
FIB Projections
Updates and Churn
Conclusions

## Slide 18: The 20-Year View of IPv6

## Slide 19: IPv6 in 2025

## Slide 20: IPv6 in 2025
AS60539, Huicast Telecom, HK

## Slide 21: More Specifics in IPv6
45% of all IPv6 prefixes are /48’s
IPv6
IPv4

## Slide 22: 20-Year IPv6 Advertised Address Span

## Slide 23: IPv6 Advertised Address Span in 2025

## Slide 24: IPv6 Advertised Address Span in 2025
26-Mar AS3462, HiNet, TW, -2K
13-Jun AS60262, PANQ, NL, -784
AS3969, MTL, MW, -356
AS204790, FLOCCUS, NL -200
10-Oct AS11492, Cable One, US, +4K

## Slide 25: IPv6 in 2025
Overall IPv6 Internet growth in terms of BGP FIB size is still increasing, and is currently at some 20,000 route entries p.a. (10%)
The advertised address span grew by just 4K /32s (thanks to Cable One!)
There were 2096 new AS’s advertising IPv6 prefixes through 2025, and 956 AS’s ceased advertising IPv6 prefixes
IPv6 is still expanding – slowly!

## Slide 26: This presentation
IPv4 Routing Table
IPv6 Routing Table
FIB Projections
Updates and Churn
Conclusions

## Slide 27: V4 BGP Table Size Predictions
Year RIB Size Prediction
2019 760,000
2020 814,000
2021 856,000
2022 906,000
2023 942,000
2024 944,000
2025 996,000 994,000
2026 1,040,000 1,101,000
2027 1,035,000
2028 1,048,000
2029 1,057,000
2030 1,060,000
Predictive uncertainty

## Slide 28: V4 BGP Table Size Predictions
Year RIB Size Prediction
2019 760,000
2020 814,000
2021 856,000
2022 906,000
2023 942,000
2024 944,000
2025 996,000 994,000
2026 1,040,000 1,101,000
2027 1,035,000
2028 1,048,000
2029 1,057,000
2030 1,060,000
Predictive uncertainty
2025 saw a higher growth than a polynomial model would predict
The best fit over the past 5 years is still a polynomial model, but the best fit over the past 3 years is a linear model

## Slide 29: V6 BGP Table Size Predictions
Year RIB Size
2019 62,000
2020 79,000
2021 106,000
2022 147,000
2023 172,000
2024 201,000
2025 222,000
2026 250,000 245,000 254,000
2027 271,000 286,000
2028 296,000 319,000
2029 322,000 353,000
2030 348,000 388,000
Linear O(2) Poly
Note that the IPv6 tables are 128bits wide – i.e. 4x the size of the IPv4 tables!

## Slide 30: V6 BGP Table Size Predictions
Year RIB Size
2019 62,000
2020 79,000
2021 106,000
2022 147,000
2023 172,000
2024 201,000
2025 222,000
2026 250,000 245,000 254,000
2027 271,000 286,000
2028 296,000 319,000
2029 322,000 353,000
2030 348,000 388,000
Linear O(2) Poly
Note that the IPv6 tables are 128bits wide – i.e. 4x the size of the IPv4 tables!
The growth model for IPv6 is highly uncertain today – It looks like a linear growth model matches the most recent 24 months of data
The underlying network growth is lower, and over half of the growth in this model is due to the continued intensive use of /48 more specifics

## Slide 31: BGP Table Growth
The good news …
  As long as we are prepared to live within the technical constraints of the current routing paradigm, the Internet’s use of BGP will continue to be viable for some time yet

## Slide 32: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Conclusions

## Slide 33: IPv4 BGP Updates – Daily Updates

## Slide 34: IPv4 BGP Updates – Daily Updates
The IPv4 network is surprisingly stable
The number of withdrawals per day has been relatively steady for some 15 years (aside from some increases in 2022/3)
The number of updates per day has been steady through 2025

## Slide 35: IPv4 Unstable Prefixes per Day

## Slide 36: IPv4 Unstable Prefixes per Day
The number of prefixes that are the subject of updates has been slowly increasing over this 15-year period
The rate of increase of unstable prefixes is far lower than the number of advertised prefixes

## Slide 37: IPv4 BGP Convergence Performance

## Slide 38: IPv4 BGP Convergence Performance
Convergence performance has been steady for 15 years, despite the massive growth in the network
The IPv4 network topology continues to increase in density, keeping critical AS Paths short as the network itself increases in size

## Slide 39: Updates in IPv4 BGP
The IPv4 inter-domain routing system is still highly stable …
The number of updates per instability event and the time to converge to a stable forwarding state has been relatively constant for many years
20% of prefixes generate 77% of all updates. Less than 5% of all origin networks are linked to 78% of all updates. Routing instability is concentrated in a small number of highly unstable cases.

## Slide 40: V6 BGP Updates
LOG Scale!

## Slide 41: V6 BGP Updates
LOG Scale!
The growth trajectory of IPv6 updates has stopped, and the daily total of updates and withdrawals has been steady across 2025

## Slide 42: V6 Unstable Prefixes
LOG Scale!

## Slide 43: V6 Unstable Prefixes
LOG Scale!
The number of unstable address prefixes has stabilised since 2023
Proportionally, IPv6 prefixes are ~2x more likely to be updated as compared to IPv4 prefixes

## Slide 44: V6 Convergence Performance

## Slide 45: V6 Convergence Performance
Time to converge has been very unstable for years in IPv6
This is now stabilising to a level that is on a par with the IPv4 network

## Slide 46: Updates in IPv6 BGP
Compared to IPv4, the IPv6 network has exhibited a high level of skew of routing instability, where a small number of networks contribute disproportionately to the overall level of BGP updates in IPv6.
Just 3 AS’s generated 20% of the BGP IPv6 update load in early December 2025. IPv6 routing instability is still concentrated in a small number of pathologically unstable cases.
https://www.potaroo.net/bgpupds/reports/v6-bgpupd.html

## Slide 47: The Highlights
IPv4 FIB Summary
IPv6 FIB Summary
FIB Projections
Churn
Conclusions

## Slide 48: Routing Futures
There is no further acute scaling pressure from BGP as a routing protocol – the relatively compressed inter-AS topology and stability of the infrastructure links tend to ensure that BGP remains effective in routing the internet.
Instability levels are high, generally driven by a small set of highly unstable “super update generators”

## Slide 49: Routing Futures
The frenetic pace of expansion in the routing infrastructure of the Internet has slowed down in recent years. The IPv4 BGP network grew slightly in 2025, while IPv6 FIB size growth has slackened off
The drivers for growth were the product of the population of networks with discrete routing policies and the need to balance incoming traffic across multiple paths (traffic engineering) – the rapid increase in the use of CDN platforms has reduced the dependence on transit routes to provide content and services to end users.
Much of the overall volume of long-haul traffic has shifted to privately operated cloud platforms, and the demands on the public routed common infrastructure are in relative decline

## Slide 50: Some Practical Suggestions
For those network operators whose service needs are dependent on the BGP network to some extent (which is mostly everyone)
Know your network’s limits:
Understand your routing FIB capacity in the default-free parts of your network
There may be some default max prefix setting of ~1M FIB entries which will cause a BGP session shutdown when tripped
  AS 4804 (Optus) in Australia appeared to encounter this situation in October 2023
Use a max prefix exceeded setting which avoids session shutdown where possible

## Slide 51: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Review your IPv4 / IPv6 portioning in the FIB tables - a dual-stack eBGP router will conservatively need a 1.2 M 32-bit IPv4 slots and 350K 128-bit IPv6 slots for a full eBGP routing table in line cards by 2026 if they are using a complete uncompressed eBGP FIB load (plus internal routes of course). That’s roughly the same memory footprint for IPv4 and IPv6!

## Slide 52: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Default routes can be helpful
Judicious use of default routes in your internal network may allow you drop this high-speed line card memory requirement significantly

## Slide 53: Some Practical Suggestions
Know your network’s limits
Review your routers’ settings
Default routes can be helpful
Time for hot caching in line card FIBs?
Using a hot cache for line card FIB cache would reduce the high-speed TCAM memory requirement significantly without visible performance cost

## Slide 54: That’s it!
Questions?